## Slide 1: Deep Neural Network On FPGA Midterm Presentation
Students:
Amit Shtober
Alon Nemirovsky
Supervisors:
Ina Rivkin
Oz Shmueli
Winter 2020-2021

## Slide 2: Project Goals
Evaluate and validate the Xilinx Vitis-AI ecosystem :
  1. Understanding Vitis-AI ecosystem
  2. Running full flow from TensorFlow to the FPGA
    Step #1 – Using trained model from Xilinx Zoo (resnet50)
    Step #2 – Using untrained model from the Zoo (MNIST), Modify it and run the flow in order to fully understand the ecosystem ability
  3. Evaluate and modify, when possible, each step in the process of the ecosystem
  4. Creating a tutorial for running the flows step by step and indicate problems we have encountered in the process

## Slide 3: Deep Neural Network
Creation of Neural Network was inspired by the human brain and the way it functions
Works according to the algorithm and can predict a solution based on experience
The system has process layers that indicates on the depth of the Neural Network
This method is very popular and highly used today

## Slide 4: Creating The Network
Full process of creating working neural network Includes:
  Creating the model
  Train it using CPU/GPU
  Optimize the model
  Inference which can be done on various machines such as host using GPU or dedicated Hardware
  Create and manufacture the dedicated hardware which will run the Inference stage

## Slide 5: Vitis-AI Ecosystem
Xilinx offers a full ecosystem which helps deal with those problems. It includes:
  Dedicated IP which called DPU
  AI Zoo - Repository which includes optimized deep learning models. Great for quick start
  Quantizer - Takes a floating-point model and performs pre-processing and then quantizes the weights/biases and activations to the given bit width
  Compiler - Maps a network model into a highly optimized DPU instruction sequence

## Slide 6
An integrated circuit designed to be configured by a designer using HDL
Great for parallel tasks (adders and multipliers)
ZCU104 evaluation board
UART
SD CARD
PL - FPGA
PS - ARM® Cortex™-A53 processor
ETHERNET
ZCU104
evaluation
board
DDR4
USB

## Slide 7: Full Flow - Block Diagram
Host code
VART based code, send instructions to the DPU
Untrained Model
Quantized Model
Kernel code
Compiled Model DPU instruction set
Trained Model
Train using
Tensorflow
V-AI Quantizer
V-AI Compiler
Xilinx Zoo
Fetch trained
Model
DPUS run the DPU instructions
ARM run the host code
(also: CPU kernel instructions)
ZCU104 evaluation board
Transfer to the Host Code
The DPU IP Uploaded as a bitfile to the FPGA during board booting, using the SD CARD slot
DPU Verilog Xilinx IP
DPU kernel instructions
Results

## Slide 8: Progress Status (1/2)
Setting up a VM with ubuntu using VMware
Initialize docker environment on the VM in order to use an exists image with Xilinx tools
  Demands large storage
  VirtualBox does not support FMA instructions, switched to VMware
Setting up the evaluation board
  Flash the OS image and bit-file into the SD card and upload it to the evaluation board
Taking resnet-50 frozen model from Xilinx zoo, quantize and compile it using Xilinx tools and Running it on the board

## Slide 9: Progress Status (2/2)
Create new model from scratch in TS and freeze it
  Freezing the model in TS is complex. Demanded research in order to find a suitable way to do it
Quantize and Compile the model using Xilinx tools
  The model output files works only using TensorFlow 1.x
  The ecosystem having trouble use fully connected layers, therefore we used convolution layers
  Dense-softmax layer failed in quantization stage. Used sigmoid layer as a workaround
  The sigmoid layer couldn’t run on the DPU, only on the CPU
Create python Host script to run the model on the DPU/CPU
Running the model on the board

## Slide 10
Freezing the model
Running the model on the board CPU

## Slide 11: MNIST Classification Model
The MNIST handwritten digits dataset is a publicly available dataset that contains a total of 70k 8bit grayscale images each of which are 28pixels x 28pixels

## Slide 12: CNN

## Slide 13: Flow Demonstration

## Slide 14: What’s Next
Analyze the problems we faced so far in order to understand the cause and to investigate the limitation of the ecosystem
Modify parameters in the ecosystem in order to check the ecosystem robustness
Evaluate the inference performance of the board against the CPU
Fully understand the host code and the consequences of running some layers on the CPU and some on the DPU
Research about the DPU block design: fetch the RTL code from GitHub, Analyze and compile it
Complete the word tutorial

## Slide 15: Schedule
Duration | Start Date | Task
Week | 21.10.20 | Reach basic understanding the product and its capabilities
Two and half weeks | 28.10.20 | Creating a Working environment for the tools
Two weeks | 15.11.20 | Running full procedure on the model resnet50 from Xilinx Zoo to the Board
3-4 weeks | 7.12.20 | Running full procedure on the model resnet50 from Tensorflow Zoo to the Board
Two weeks | 4.1.21 | Analyze problems and Modify parameters in the ecosystem
week | 11.1.21 | Evaluate the inference performance
week | 18.1.21 | Fully understand the host code and Research about the DPU block design